## Slide 1: YOU’RE
A Device to Control M$ Teams
ON MUTE!
Paul Harvey

## Slide 2: Components of the Solution
Cycle
Windows
Toggle
Mute
Toggle
Camera
101010010101
External
Wireless
PC software to
control teams
protocol
hardware

## Slide 3: Hardware - Microcontroller
C++
Arduino Nano
Compile
Upload
ATmega328 Microcontroller
32K Flash
2K DRAM
14 digital I/O pins
8 Analogue I/O pins
40 mA per pin
Monitor switch pins
Marshall/send protocol
Update display
Play tones
De-marshall protocol and dispatch

## Slide 4: Hardware - Schematic
Arduino Nano
R1, R2, R3 - Pulldown resistors
P1 – LCD contrast
R4, R5 - Voltage divider
R6 - Current limiting resistor for LED backlight
S1 – Cycle
S2 – Mute
S3 - Camera
J1 – Piezo buzzer
LCD
Bluetooth/ HC-05

## Slide 5: Hardware - Reality
Arduino Nano
P1 – LCD contrast
R4, R5 - Voltage divider
R1, R2, R3 - Pulldown resistors
R6 - Current limiting resistor for LED backlight
S1 – Cycle
S2 – Mute
S3 - Camera
J1 – Piezo buzzer
Bluetooth/ HC-05
LCD

## Slide 6: Protocol
Offset | 0 | 1 | 2…n
Function | Length | OpCode | Payload
Packet Structure
Operations
OpCode | Name | In/Out | Payload | Description
0x01 | Cycle Windows | Out | - | Cycle Teams windows to the front.
0x02 | Toggle Mute | Out | - | Toggle microphone mute
0x03 | Toggle Video | Out | - | Toggle video camera
0x04 | Error | In | - | An error condition has occurred
0xFF | Debug | Out | String | Send a debug message

## Slide 7: PC Software
C#
Pair and connect Ardiuno via BT
De-marshall protocol and dispatch
Interact with Teams to cycle windows/toggle mute/toggle camera

## Slide 8: Tracing an Example
+5V
+5V
0V
ATMega328
1
2
3
4
4
0x01 0x01
HC-05

## Slide 9
Demo

## Slide 10: Bill of Materials
Component | # | Total Cost
Arduino Nano | 1 | £5.66
LCD Display | 1 | £3.99
Resistors | 4 | £0.04
Potentiometer | 1 | £0.07
Switch | 3 | £0.09
Piezo Buzzer | 1 | £0.50
Wired/USB
Wireless/Bluetooth
Component | # | Total Cost
HC-05 | 1 | £4.80
Resistors | 2 | £0.02
Component | # | Total Cost
Buck Converter | 1 | £2.33
Battery Power
Approx. £10.00

## Slide 11: Try Yourself?
Arduino
Starter
Kit
The