## Slide 1: YOU’RE
A Device to Control M$ Teams
ON MUTE!
Paul Harvey
Notes: Often find myself doing other things during Teams meetings.
Then struggle to find the right Teams Window / unmute when suddenly needed.
This project developers a – maybe the not most straightforward! – solution to the problem.

## Slide 2: Components of the Solution
Cycle
Windows
Toggle
Mute
Toggle
Camera
101010010101
External
Wireless
PC software to
control teams
protocol
hardware
Notes: Approach is to:
Create some hardware that is sat on the desk to control teams:
  Functions to:
    Cycle windows to front
    Toggle mute
    Toggle camera
  Then this is always available no matter what is happening on the desktop
  Maybe with some display/audio to give feedback.
Device would communicate wirelessly with the computer running Teams
  Using some protocol, I need to define
A software agent on the PC running Teams would listen to this protocol and control Team appropriately.

## Slide 3: Hardware - Microcontroller
C++
Arduino Nano
Compile
Upload
ATmega328 Microcontroller
8bit @ 16MHz
32K Flash
2K DRAM
14 digital I/O pins
8 Analogue I/O pins
40 mA per pin
Monitor switch pins
Marshall/send protocol
Update display
Play tones
De-marshall protocol and dispatch
Notes: Hardware based around a Microcontroller
The old familiar Arduino (nano)
  Go through specs
Aside Microcontroller vs Microprocessor, Arduino vs Raspberry Pi
  Both capable of running a machine code programme
  PI is full blown computer with a full operating system
  Arduino just has a boot loader, and you are writing on the metal
  PI can deliver maybe - 16mA per pin max not exceeding a total of 50mA
  Arduino more like 40mA per pin max total 200mA max
  So can drive a lot more directly from the Arduino
  Arduino pushes C/C++ as Dev language as opposed to Python on the Pi
  Arduino – simpler/less poweful and cheaper
  Arduino – fewer interfaces – typically just USB
  PI – typically WiFi, ethernet, several USB, HDMI
Process
  Develop program on a PC
  Compile
  Upload machine code to Microcontroller
  Microcontroller will continue to run it while powered on (persistent through power cycles)
Explain the list of typical activities the code would do

## Slide 4: Hardware - Schematic
Arduino Nano
R1, R2, R3 - Pulldown resistors
P1 – LCD contrast
R4, R5 - Voltage divider
R6 - Current limiting resistor for LED backlight
S1 – Cycle
S2 – Mute
S3 - Camera
J1 – Piezo buzzer
LCD
Bluetooth/ HC-05
Notes: This shows a schematic of the core of the circuit (sans details of the power supply)
List major components
  Arduino/microcontroller
  Switches to trigger actions
  LCD for visual feedback
  Piezo for audio feedback
  Bluetooth board (HC-05)
Other items of note:
  Pull down resistors (R1, R2, R3)
    Data pins associated with switches held a ground
    Closing switch pulls them high to be detected in code
    Pull down resistor prevents short to ground!
  Potentiometer P1
    Controls contrast
  Voltage divider R4, R5
    Arduino pins are high a +5V
    HC-05 expects 3.3V
    Voltage divider does the trick
  Resistor R6
    Current limiting for LED backlight

## Slide 5: Hardware - Reality
Arduino Nano
P1 – LCD contrast
R4, R5 - Voltage divider
R1, R2, R3 - Pulldown resistors
R6 - Current limiting resistor for LED backlight
S1 – Cycle
S2 – Mute
S3 - Camera
J1 – Piezo buzzer
Bluetooth/ HC-05
LCD
Notes: This is what the circuit looks like on a breadboard.
Point out some of the major components.

## Slide 6: Protocol
Offset | 0 | 1 | 2…n
Function | Length | OpCode | Payload
Packet Structure
Operations
OpCode | Name | In/Out | Payload | Description
0x01 | Cycle Windows | Out | - | Cycle Teams windows to the front.
0x02 | Toggle Mute | Out | - | Toggle microphone mute
0x03 | Toggle Video | Out | - | Toggle video camera
0x04 | Error | In | - | An error condition has occurred
0xFF | Debug | Out | String | Send a debug message
Notes: Next piece of the puzzle is a protocol to communicate between the Microcontroller and the PC
Explain packet structure
Explain each message/opcode

## Slide 7: PC Software
C#
Pair and connect Ardiuno via BT
De-marshall protocol and dispatch
Interact with Teams to cycle windows/toggle mute/toggle camera
Notes: PC Software is other end of the protocol, acting on instructions from the Arduino and controlling Teams
Talk through the bullet points on the major actions of the software.

## Slide 8: Tracing an Example
+5V
+5V
0V
ATMega328
1
2
3
4
5
0x01 0x01
HC-05
4
Notes: Let’s follow through an example.
1. Cycle window button pressed
2. Pulls the relevant pin on the microcontroller high
3. The code detects this
  Sends the appropriate data packet to the HC-05
  We also send a message to the LCD and play a sound on the hardware
4. The HC-05 forwards this via BT to the PC
5. The software agent on the PC reads in the packet
  Decodes the packet
  Takes appropriate action against Teams
  In this case cycling the windows

## Slide 9
Demo

## Slide 10: Bill of Materials
Component | # | Total Cost
Arduino Nano | 1 | £5.66
LCD Display | 1 | £3.99
Resistors | 4 | £0.04
Potentiometer | 1 | £0.07
Switch | 3 | £0.09
Piezo Buzzer | 1 | £0.50
Wired/USB
Wireless/Bluetooth
Component | # | Total Cost
HC-05 | 1 | £4.80
Resistors | 2 | £0.02
Component | # | Total Cost
Buck Converter | 1 | £2.33
Battery Power
Approx. £10.00
Notes: This is how much it all costs
You might be able to get things a little cheaper via Ebay if you are prepared to wait!
Explain the 3 different tables.

## Slide 11: Try Yourself?
Arduino
Starter
Kit
The
Notes: If I have whetted your appetite for playing with hardware
I can recommend with the Arduino starter kit
  It requires very little knowledge of electronics
  Real projects talked through in the projects book
  Everything you need is in the kit
  Components of these can be built into more ambitious ideas
  Get’s you into building
In fact, you could build a USB (not BT) version of the above with it.
It is great fun!