## Slide 1: YOU’RE
A Device to Control M$ Teams
ON MUTE!
Paul Harvey
Notes: Often find myself doing other things during Teams meetings.
Then struggle to find the right Teams Window / unmute when suddenly needed.
This project developers a – maybe the not most straightforward! – solution to the problem.

## Slide 2: Components of the Solution
Cycle
Windows
Toggle
Mute
Toggle
Camera
101010010101
External
Wireless
PC software to
control teams
protocol
hardware
Notes: Approach is to:
Create some hardware that is sat on the desk to control teams:
  Functions to:
    Cycle windows to front
    Toggle mute
    Toggle camera
  Then this is always available no matter what is happening on the desktop
  Maybe with some display/audio to give feedback.
Device would communicate wirelessly with the computer running Teams
  Using some protocol, I need to define
A software agent on the PC running Teams would listen to this protocol and control Team appropriately.

## Slide 3: Hardware - Microcontroller
C++
ATMega328
Compile C/C++
Upload Machine Code
ATMega328 Microcontroller (µC)
8bit @ 16MHz
32K Flash
2K RAM
14 Digital I/O pins
8 Analogue I/O pins
40 mA per pin
Initialize Devices
Monitor switch pins
Marshall/send protocol
Drive display
Play tones
De-marshall protocol and dispatch
Notes: Hardware based around a Microcontroller
The old familiar Arduino (nano)
  Go through specs
Aside Microcontroller vs Microprocessor
  Both capable of running a machine code programme
  PI is full blown computer with a full operating system
  Arduino just has a boot loader, and you are writing on the metal
  PI can deliver maybe - 16mA per pin max not exceeding a total of 50mA
  Arduino more like 40mA per pin max total 200mA max
  So can drive a lot more directly from the Arduino
  Arduino pushes C/C++ as Dev language as opposed to Python on the Pi
  Arduino – simpler/less poweful and cheaper
  Arduino – fewer interfaces – typically just USB
  PI – typically WiFi, ethernet, several USB, HDMI
Process
  Develop program on a PC in C/C++
  Compile
  Upload machine code to Microcontroller
  Microcontroller will continue to run it while powered on (persistent through power cycles)
Explain the list of typical activities the code would do

## Slide 4: Hardware - Schematic
Triggering Actions
S1, S2, S3 – Tactile switches closing pulls the relevant pin high.
R1, R2, R3 – Pull down resistors
Activity LED
LED1 – Flashed by bootloader on activity
R8 – Current limiting resistor
Microcontroller
IC1 – ATMega328 µC
Runs uploaded machine code
Reacts to inputs pins
Sets output pins
Microcontroller Clock
C1, C2 and Y1 - Crystal circuit providing clock timing for the µC
Reset Switch
R7 – Pull up resistor
S4 – Reset switch triggers reset by pulling RST pin low
Visual Feedback
LCD1 - JHD659 LCD Screen
P1 - Adjusts Contrast
R6 - Current limiting resistor for LED backlight
Data lines etc. from µC
Bluetooth Communications
BT1 – HC05 Serial to Bluetooth interface
R4, R5 – Voltage divider, ATMega uses 5V logic, BT card users 3.3V
USB Comms & Uploading
FTDI1 - FT232RL serial to USB conversion
Connected to Rx/Tx lines on µC
DTR pulled low on new session – used to trigger bootloader
Audio Feedback
J1 – Piezo “speaker”
ATMega328
µC
JHD659
LCD
Screen
FTDI
FT232RL
HC05
Serial - BT
Notes: This shows a schematic of the core of the circuit (sans details of the power supply)
Talk through each of the blocks
Power – USB, 5V or battery via Buck converter

## Slide 5: Hardware - Reality
IC1 ATMega328
P1 LCD contrast
R4, R5 - Voltage divider
J1 Piezo speaker
C1, C2 and Y1 Clock circuit
S1, S2, S3 Action switches
Bluetooth HC-05
LCD1 LCD Screen
USB FT232RL
R1, R2, R3 Pull down resistors
S4, R7 Reset switch & pull up resistor
LED1 Activity LED
Notes: This is what the circuit looks like on a breadboard.
Point out some of the major components.

## Slide 6: Protocol
Offset | 0 | 1 | 2…n
Function | Length | OpCode | Payload
Packet Structure
Operations
OpCode | Name | In/Out | Payload | Description
0x01 | Cycle Windows | Out | - | Cycle Teams windows to the front.
0x02 | Toggle Mute | Out | - | Toggle microphone mute
0x03 | Toggle Video | Out | - | Toggle video camera
0x04 | Error | In | - | An error condition has occurred
0xFF | Debug | Out | String | Send a debug message
Notes: Next piece of the puzzle is a protocol to communicate between the Microcontroller and the PC
Explain packet structure
Explain each message/opcode

## Slide 7: PC Software
C#
Pair and connect external device via BT
Listen for incoming protocol de-marshall protocol and dispatch
Interact with Teams to cycle windows/toggle mute/toggle camera
Send error conditions back to external device
Notes: PC Software is other end of the protocol, acting on instructions from the Arduino and controlling Teams
Talk through the bullet points on the major actions of the software.

## Slide 8: Tracing an Example
+5V
+5V
0V
ATMega328
1
2
3
4
6
0x01 0x01
HC-05
4
7
5
Notes: Let’s follow through an example.
1. Cycle window button pressed
2. Pulls the relevant pin on the microcontroller high
3. The code detects this
  Sends the appropriate data packet to the HC-05
  We also send a message to the LCD and play a sound on the hardware
4. The HC-05 forwards this via BT to the PC
5. The software agent on the PC reads in the packet
  Decodes the packet
  Takes appropriate action against Teams
  In this case cycling the windows

## Slide 9
Demo

## Slide 10: Bill of Materials
Component | # | Total Cost
ATMega328 | 1 | £2.28
LCD Display | 1 | £3.99
Crystal | 1 | £0.12
Resistors | 6 | £0.06
Potentiometer | 1 | £0.07
Capacitors | 3 | £0.12
Switches | 4 | £0.12
Piezo Buzzer | 1 | £0.50
LED | 1 | £0.03
Core
Bluetooth
Component | # | Total Cost
HC-05 | 1 | £4.80
Resistors | 2 | £0.02
£4.82
USB
Component | # | Total Cost
FTDI FT232RL | 1 | £3.30
Capacitor | 1 | £0.04
£3.34
£7.29
Component | # | Total Cost
Buck Converter | 1 | £2.33
Battery Power
£2.33
Notes: This is how much it all costs
You might be able to get things a little cheaper via Ebay if you are prepared to wait!
Explain the 3 different tables.

## Slide 11: Try Yourself?
Arduino
Starter
Kit
The
Notes: If I have whetted your appetite for playing with hardware
You might have hear of an Arduino?
  The ATMega328 is at the heart of the Ardruino
  Plus it offers all the supporting circuitry needed to get it going and more.
I can recommend with the Arduino starter kit
  It requires very little knowledge of electronics
  Real projects talked through in the projects book
  Everything you need is in the kit
  Components of these can be built into more ambitious ideas
  Get’s you into building
In fact, you could build a USB (not BT) version of the above with it.
It is great fun!